THIS IS A PRACTICE ASSESSMENT. Show formulas, substitutions, answers (in spaces provided) and units!

1.	A 3.25-V battery is used to fully charge a 725 (F capacitor. How much charge was transferred from the negative to the positive plate?						1. _________________

Three 725 (F capacitors are connected in parallel to a 3.25 V battery.

2.	What is the equivalent capacitance?						2. _________________

3.	What is the charge on each capacitor?					3. _________________

Three 725 (F capacitors are connected in series to a 3.25 V battery.

4.	What is the equivalent capacitance?						4. _________________

5.	What is the voltage on each capacitor?					5. _________________

A 725 (F capacitor will be manufactured using a dielectric having a permittivity of 4.50 (0 and circular plates having a diameter of 0.750 cm.

6.	What should the plate separation (and the thickness of the dielectric) be? 	6. _________________

7.	Is it likely that this large a capacity could be constructed using parallel plate architecture? ___ Why?

__________________________________________________________________________________

The following question is about the electrical energy stored in a capacitor.

8.	Find the energy stored in a 725 (F capacitor charged up to 3.25 V.		8. _________________

C1 is initially charged to 3.25 V. C2 is initially uncharged.

9.	What is the charge on C1’s plates?			9. _________________

10.	The switch is closed, connecting C1 to C2. What is the new charge on the plates of C1?					10. _________________

The following question is about a charging RC circuit. The capacitor is initially uncharged.

11.	Make a sketch graph showing the family of curves representing the voltage across the capacitor after the switch is closed and as RC increases. Show at least three different RC curves, and label them “low,” medium,” and “high.”              11._in sketch_

A circuit constructed of a resistor R and a capacitor C has a switch which can be made to charge and discharge the capacitor.

12.	Label the switch position which charges the capacitor with an “A” at the small circle in the schematic.            12._in diagram_

13.	Label the switch position which discharges the capacitor with a “B” at the small circle in the schematic.         13._in diagram_

14.	Draw arrows in the discharge loop showing the direction of current flow during discharge.		   14._in diagram_

15.	What equation does Kirchhoff’s rule for V produce during discharge? Your final equation should have only these variables: q, (q, (t, R and C.

15. ________________

A 725 (F capacitor is charged to 2.35 V. It is then discharged through a 15.0 M( resistor.

16. Find the time constant.							16. ________________

17.	Find the initial charge on the plates.						17. ________________

18.	Find the charge on the plates exactly three time constants after discharge has begun.

18. ________________

19.	Find the capacitor’s voltage 1870 s after discharge begins. 			19. ________________

20.	Find the instantaneous current at t = 1870 s.					20. ________________

21.	Find the half-life of the capacitor’s voltage.					21. ________________

A timer using a capacitor and a resistor needs the RC circuit to have a half-life of 60.0 seconds. It will be using a capacitor of 725 (F, initially charged to a voltage of 6.25 V.

22.	What should the value of the time constant be?				22. ________________

23.	What value should the resistor have?					23. ________________

24.	What will the capacitor voltage be at this time?				24. ________________